## Slide 1: Chapter 1: Embedded Computing
Embedded System Design

## Slide 2: Microprocessor and embedded systems
Computing systems are everywhere
Most of us think of “desktop” computers
  PC’s
  Laptops
  Mainframes
  Servers
But a PC is not itself an embedded system
  Microprocessor , I/O, Memory
  The challenges are not computer engineering

## Slide 3: Microprocessor and Embedded systems
Microprocessor overview
  programmability
  4,8,16,32,64
  CISC, RISC
  Multiprocessor

## Slide 4: Embedded systems overview
Embedded computing systems
  Computing systems embedded within electronic devices
  Hard to define. Nearly any computing system other than a desktop computer
  Billions of units produced yearly, versus millions of desktop units
  Perhaps 50 per household and per automobile
Computers are in here...
and here...
and even here...
Lots more of these, though they cost a lot less each.

## Slide 5: A “short list” of embedded systems
Anti-lock brakes
Auto-focus cameras
Automatic teller machines
Automatic toll systems
Automatic transmission
Avionic systems
Battery chargers
Camcorders
Cell phones
Cell-phone base stations
Cordless phones
Cruise control
Curbside check-in systems
Digital cameras
Disk drives
Electronic card readers
Electronic instruments
Electronic toys/games
Factory control
Fax machines
Fingerprint identifiers
Home security systems
Life-support systems
Medical testing systems
Modems
MPEG decoders
Network cards
Network switches/routers
On-board navigation
Pagers
Photocopiers
Point-of-sale systems
Portable video games
Printers
Satellite phones
Scanners
Smart ovens/dishwashers
Speech recognizers
Stereo systems
Teleconferencing systems
Televisions
Temperature controllers
Theft tracking systems
TV set-top boxes
VCR’s, DVD players
Video game consoles
Video phones
Washers and dryers

## Slide 6
Definition of Embedded Systems
Embedded system: is a system whose principal function is not computational, but which is controlled by a computer embedded within it.
6

## Slide 7: characteristics of embedded systems
Single-functioned
  Executes a single program, repeatedly
Tightly-constrained
  Low cost, low power, small, fast, etc.
Reactive and real-time
  Continually reacts to changes in the system’s environment
  Must compute certain results in real-time without delay

## Slide 8: Performance of embedded systems —real-time
CPU
  SPEC, Multiprocessor,Multicore
Platform
  BUS, Memory, I/O device, etc.
Program
  Structure
Task
  Scheduling

## Slide 9: Design metrics
Obvious design goal:
  Construct an implementation with desired functionality
Key design challenge:
  Simultaneously optimize numerous design metrics
Design metric
  A measurable feature of a system’s implementation
  Optimizing design metrics is a key challenge

## Slide 10: Design metrics
Common metrics
  Unit cost: the monetary cost of manufacturing each copy of the system, excluding NRE cost
  NRE cost (Non-Recurring Engineering cost): The one-time monetary cost of designing the system
  Size: the physical space required by the system
  Performance: the execution time or throughput of the system
  Power: the amount of power consumed by the system
  Flexibility: the ability to change the functionality of the system without incurring heavy NRE cost

## Slide 11: Design metrics
Common metrics (continued)
  Time-to-prototype: the time needed to build a working version of the system
  Time-to-market: the time required to develop a system to the point that it can be released and sold to customers
  Maintainability: the ability to modify the system after its initial release
  Correctness, safety, many more

## Slide 12: Design process
Top-down / Bottom-up
  Requirements
  Specification
  Architecture
  Components
  System integration

## Slide 13: Design metric competition
Expertise with both software and hardware is needed to optimize design metrics
  Not just a hardware or software expert, as is common
  A designer must be comfortable with various technologies in order to choose the best for a given application and constraints
Size
Performance
Power
NRE cost
Microcontroller
CCD preprocessor
Pixel coprocessor
A2D
D2A
JPEG codec
DMA controller
Memory controller
ISA bus interface
UART
LCD ctrl
Display ctrl
Multiplier/Accum
Digital camera chip
lens
CCD
Hardware
Software

## Slide 14: Intel 2700G appliation–High Impact Presentation

## Slide 15: Navman iCN 630
The TFT automotive rated LCD 3.8" QVGA 320 x 240 resolution screen has more than 65,000 colours displaying maps with unprecedented clarity.
3D map views give the best perspective for the street ahead, a real help for when navigating ahead.

## Slide 16: NRE and unit cost metrics
Costs:
  Unit cost: the monetary cost of manufacturing each copy of the system, excluding NRE cost
  NRE cost (Non-Recurring Engineering cost): The one-time monetary cost of designing the system
  total cost = NRE cost + unit cost * # of units
  per-product cost = total cost / # of units
  = (NRE cost / # of units) + unit cost

## Slide 17: Three key embedded system technologies
Technology
  A manner of accomplishing a task, especially using technical processes, methods, or knowledge
Three key technologies for embedded systems
  Processor technology
  IC technology
  Design technology

## Slide 18: General-purpose processors
Programmable device used in a variety of applications
  Also known as “microprocessor”
Features
  Program memory
  General datapath with large register file and general ALU
User benefits
  Low time-to-market and NRE costs
  High flexibility
“Pentium” the most well-known, but there are hundreds of others
IR
PC
Register
file
General
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory

## Slide 19: Single-purpose processors
Digital circuit designed to execute exactly one program
  a.k.a. coprocessor, accelerator or peripheral
Features
  Contains only the components needed to execute a single program
  No program memory
Benefits
  Fast
  Low power
  Small size
Datapath
Controller
Control logic
State register
Data
memory
index
total
+

## Slide 20: Application-specific processors
Programmable processor optimized for a particular class of applications having common characteristics
  Compromise between general-purpose and single-purpose processors
Features
  Program memory
  Optimized datapath
  Special functional units
Benefits
  Some flexibility, good performance, size and power
IR
PC
Registers
Custom
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory

## Slide 21: The co-design ladder
In the past:
  Hardware and software design technologies were very different
  Recent maturation of synthesis enables a unified view of hardware and software
Hardware/software “codesign”
Implementation
Assembly instructions
Machine instructions
Register transfers
Compilers
(1960's,1970's)
Assemblers, linkers
(1950's, 1960's)
Behavioral synthesis
(1990's)
RT synthesis
(1980's, 1990's)
Logic synthesis
(1970's, 1980's)
Microprocessor plus program bits: “software”
VLSI, ASIC, or PLD implementation: “hardware”
Logic gates
Logic equations / FSM's
Sequential program code (e.g., C, VHDL)
The choice of hardware versus software for a particular function is simply a tradeoff among various design metrics, like performance, power, size, NRE cost, and especially flexibility; there is no fundamental difference between what hardware or software can implement.

## Slide 22: Homework
Why not use PCs for all Embedded computing？P7/P5
The major goals of the embedded system design? P12
多校区售饭系统
  存在问题
  网络架构
  通信方式