## Slide 1: Biography
Shen zhaoyan
(申兆岩)
2008~2012
Bachelor Degree, Shandong University
School of Computer Science and Technology
2012~2015
Master Degree, Shandong University
Computer Science, Supervisor: Zhiping Jia
2015~2018
PhD Degree, The HongKong Polythetic University
Computing, Supervisor: Zili Shao
2018~now
Assistant Professor, Shandong University
School of Computer Science and Technology
Research Interest
Embedded System，Big Data Storage
Smart Gateway, IoT Blockchain

## Slide 2: 为什么需要新型的非易失性存储器
云存储
磁盘
固态硬盘
Emerging NVM
内存
缓存
1ns
SRAM
SRAM
30ns
DRAM
>10ms
HDD
?
Notes: Emerging, resistive memory technologies (NVM) can help
Traditional memory
  Slow, high cost
  Higher energy
  Speed gap
New memory technology
  Technology scalability:
  lower cost, higher capacity,
  lower energy
  Energy (and power) efficiency
  QoS support and configurability (for consolidation)

## Slide 3: Chapter 3: CPU
Embedded System Design

## Slide 4: Selecting a Microprocessor
Issues
  Technical: speed, power, size, cost
  Other: development environment, prior expertise, licensing, etc.
Speed: how evaluate a processor’s speed?
  Clock speed – but instructions per cycle may differ
  Instructions per second – but work per instr. may differ
  Dhrystone: Synthetic benchmark, developed in 1984. Dhrystones/sec.
    MIPS: 1 MIPS = 1757 Dhrystones per second (based on Digital’s VAX 11/780). A.k.a. Dhrystone MIPS. Commonly used today.
      So, 750 MIPS = 750*1757 = 1,317,750 Dhrystones per second
  SPEC: set of more realistic benchmarks, but oriented to desktops
  EEMBC – EDN Embedded Benchmark Consortium,
    Suites of benchmarks: automotive, consumer electronics, networking, office automation, telecommunications

## Slide 5: Input and Output
Required to communicate with outside world
PC System:
  Keyboard
  Monitor
  Parallel port (printer port)
  Serial port + USB
Embedded System:
  Sensors (e.g. in automobile: acceleration sensor, seat sensor)
  Actuators (e.g. in automobile: valves for airbags)

## Slide 6: Input and Output
Input / output device implementation can be:
• Memory-mapped
• I/O mapped (ports)
• DMA (direct memory access)

## Slide 7: Parallel communication
Multiple data, control, and possibly power wires
  One bit per wire
High data throughput with short distances
Typically used when connecting devices on same IC or same circuit board
  Bus must be kept short
    long parallel wires result in high capacitance values which requires more time to charge/discharge
    Data misalignment between wires increases as length increases
Higher cost, bulky

## Slide 8: Serial communication
Single data wire, possibly also control and power wires
Words transmitted one bit at a time
Higher data throughput with long distances
  Less average capacitance, so more bits per unit of time
Cheaper, less bulky
More complex interfacing logic and communication protocol
  Sender needs to decompose word into bits
  Receiver needs to recompose bits into word
  Control signals often sent on same wire as data increasing protocol complexity

## Slide 9: Serial Transmission Using UARTs
embedded device
1
0
0
1
1
0
1
1
Sending UART
1
0
0
1
1
0
1
1
Receiving UART
1
0
0
1
1
0
1
1
start bit
data
end bit
UART: Universal Asynchronous Receiver Transmitter
  Takes parallel data and transmits serially
  Receives serial data and converts to parallel
Parity: extra bit for simple error checking
Start bit, stop bit
Baud rate
  signal changes per second
  bit rate usually higher

## Slide 10: Wireless communication
Infrared (IR)
  Electronic wave frequencies just below visible light spectrum
  Diode emits infrared light to generate signal
  Infrared transistor detects signal, conducts when exposed to infrared light
  Cheap to build
  Need line of sight, limited range
Radio frequency (RF)
  Electromagnetic wave frequencies in radio spectrum
  Analog circuitry and antenna needed on both sides of transmission
  Line of sight not needed, transmitter power determines range

## Slide 11: Error detection and correction
Often part of bus protocol
Error detection: ability of receiver to detect errors during transmission
Error correction: ability of receiver and transmitter to cooperate to correct problem
  Typically done by acknowledgement/retransmission protocol
Bit error: single bit is inverted
Burst of bit error: consecutive bits received incorrectly
Parity: extra bit sent with word used for error detection
  Odd parity: data word plus parity bit contains odd number of 1’s
  Even parity: data word plus parity bit contains even number of 1’s
  Always detects single bit errors, but not all burst bit errors
Checksum: extra word sent with data packet of multiple words
  e.g., extra word contains XOR sum of all data words in packet

## Slide 12: Serial protocols: I2C
I2C (Inter-IC)
  Two-wire serial bus protocol developed by Philips Semiconductors nearly 20 years ago
  Enables peripheral ICs to communicate using simple communication hardware
  Data transfer rates up to 100 kbits/s and 7-bit addressing possible in normal mode
  3.4 Mbits/s and 10-bit addressing in fast-mode
  Common devices capable of interfacing to I2C bus:
    EPROMS, Flash, and some RAM memory, real-time clocks, watchdog timers, and microcontrollers

## Slide 13: I2C bus structure
SCL
SDA
Micro-controller
(master)
EEPROM
(servant)
Temp. Sensor
(servant)
LCD-controller
(servant)
< 400 pF
Addr=0x01 Addr=0x02 Addr=0x03
D
C
ST
ART
A6
A5
A0
R/w
ACK
D8
D7
D0
ACK
ST
OP
From Servant
From receiver
Typical read/write cycle
SDA
SCL
SDA
SCL
SDA
SCL
SDA
SCL
Start condition
Sending 0
Sending 1
Stop condition

## Slide 14: Serial protocols: CAN
CAN (Controller area network)
  Protocol for real-time applications
  Developed by Robert Bosch GmbH
  Originally for communication among components of cars
  Applications now using CAN include:
    elevator controllers, copiers, telescopes, production-line control systems, and medical instruments
  Data transfer rates up to 1 Mbit/s and 11-bit addressing
  Common devices interfacing with CAN:
    8051-compatible 8592 processor and standalone CAN controllers
  Actual physical design of CAN bus not specified in protocol
    Requires devices to transmit/detect dominant and recessive signals to/from bus
    e.g., ‘1’ = dominant, ‘0’ = recessive if single data wire used
    Bus guarantees dominant signal prevails over recessive signal if asserted simultaneously

## Slide 15: Serial protocols: FireWire
FireWire (a.k.a. I-Link, Lynx, IEEE 1394)
  High-performance serial bus developed by Apple Computer Inc.
  Designed for interfacing independent electronic components
    e.g., Desktop, scanner
  Data transfer rates from 12.5 to 400 Mbits/s, 64-bit addressing
  Plug-and-play capabilities
  Packet-based layered design structure
  Applications using FireWire include:
    disk drives, printers, scanners, cameras
  Capable of supporting a LAN similar to Ethernet
    64-bit address:
      10 bits for network ids, 1023 subnetworks
      6 bits for node ids, each subnetwork can have 63 nodes
      48 bits for memory address, each node can have 281 terabytes of distinct locations

## Slide 16: Serial protocols: USB
USB (Universal Serial Bus)
  Easier connection between PC and monitors, printers, digital speakers, modems, scanners, digital cameras, joysticks, multimedia game equipment
  2 data rates:
    12 Mbps for increased bandwidth devices
    1.5 Mbps for lower-speed devices (joysticks, game pads)
  Tiered star topology can be used
    One USB device (hub) connected to PC
      hub can be embedded in devices like monitor, printer, or keyboard or can be standalone
    Multiple USB devices can be connected to hub
    Up to 127 devices can be connected like this
  USB host controller
    Manages and controls bandwidth and driver software required by each peripheral
    Dynamically allocates power downstream according to devices connected/disconnected

## Slide 17: Parallel protocols: PCI Bus
PCI Bus (Peripheral Component Interconnect)
  High performance bus originated at Intel in the early 1990’s
  Standard adopted by industry and administered by PCISIG (PCI Special Interest Group)
  Interconnects chips, expansion boards, processor memory subsystems
  Data transfer rates of 127.2 to 508.6 Mbits/s and 32-bit addressing
    Later extended to 64-bit while maintaining compatibility with 32-bit schemes
  Synchronous bus architecture
  Multiplexed data/address lines

## Slide 18: Parallel protocols: ARM Bus
ARM Bus
  Designed and used internally by ARM Corporation
  Interfaces with ARM line of processors
  Many IC design companies have own bus protocol
  Data transfer rate is a function of clock speed
    If clock speed of bus is X, transfer rate = 16 x X bits/s
  32-bit addressing

## Slide 19: Wireless protocols: IrDA
IrDA
  Protocol suite that supports short-range point-to-point infrared data transmission
  Created and promoted by the Infrared Data Association (IrDA)
  Data transfer rate of 9.6 kbps and 4 Mbps
  IrDA hardware deployed in notebook computers, printers, PDAs, digital cameras, public phones, cell phones
  Lack of suitable drivers has slowed use by applications
  Windows 2000/98 now include support
  Becoming available on popular embedded OS’s

## Slide 20: Wireless protocols: Bluetooth
Bluetooth
  New, global standard for wireless connectivity
  Based on low-cost, short-range radio link
  Connection established when within 10 meters of each other
  No line-of-sight required
    e.g., Connect to printer in another room

## Slide 21: Wireless Protocols: IEEE 802.11
IEEE 802.11
  Proposed standard for wireless LANs
  Specifies parameters for PHY and MAC layers of network
    PHY layer
      physical layer
      handles transmission of data between nodes
      provisions for data transfer rates of 1 or 2 Mbps
      operates in 2.4 to 2.4835 GHz frequency band (RF)
      or 300 to 428,000 GHz (IR)
    MAC layer
      medium access control layer
      protocol responsible for maintaining order in shared medium
      collision avoidance/detection

## Slide 22: Microprocessor interfacing: interrupts
What is the address (interrupt address vector) of the ISR?
  Fixed interrupt
    Address built into microprocessor, cannot be changed
    Either ISR stored at address or a jump to actual ISR stored if not enough bytes available
  Vectored interrupt
    Peripheral must provide the address
    Common when microprocessor has multiple peripherals connected by a system bus
  Compromise: interrupt address table

## Slide 23: Interrupt-driven I/O using vectored interrupt
1(a): μP is executing its main program.
1(b): P1 receives input data in a register with address 0x8000.
2: P1 asserts Int to request servicing by the microprocessor.
3: After completing instruction at 100, μP sees Int asserted, saves the PC’s value of 100, and asserts Inta.
5(a): μP jumps to the address on the bus (16). The ISR there reads data from 0x8000, modifies the data, and writes the resulting data to 0x8001.
6: The ISR returns, thus restoring PC to 100+1=101, where μP resumes executing.
5(b): After being read, P1 deasserts Int.
Time
4: P1 detects Inta and puts interrupt address vector 16 on the data bus.

## Slide 24: Interrupt-driven I/O using vectored interrupt
μP
P1
P2
System bus
Data memory
0x8000
0x8001
16:
MOV R0, 0x8000
17:
# modifies R0
18:
MOV 0x8001, R0
19:
RETI # ISR return
ISR
100:
101:
instruction
instruction
...
Main program
...
Program memory
PC
100
Int
Inta
16
1(a): P is executing its main program
1(b): P1 receives input data in a register with address 0x8000.

## Slide 25: Intel 8259 programmable priority controller
Intel 8259
D[7..0]
A[0..0]
RD
WR
INT
INTA
CAS[2..0]
SP/EN
IR0
IR1
IR2
IR3
IR4
IR5
IR6
IR7

## Slide 26
几个中断概念

## Slide 27: Pipelining: Increasing Instruction Throughput
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Fetch-instr.
Decode
Fetch ops.
Execute
Store res.
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Wash
Dry
Time
Non-pipelined
Pipelined
Time
Time
Pipelined
pipelined instruction execution
non-pipelined dish cleaning
pipelined dish cleaning
Instruction 1

## Slide 28: Superscalar and VLIW Architectures
Performance can be improved by:
  Faster clock (but there’s a limit)
  Pipelining: slice up instruction into stages, overlap stages
  Multiple ALUs to support more than one instruction stream
    Superscalar
      Scalar: non-vector operations
      Fetches instructions in batches, executes as many as possible
        May require extensive hardware to detect independent instructions
      VLIW: each word in memory has multiple independent instructions
        Relies on the compiler to detect and schedule instructions
        Currently growing in popularity

## Slide 29: Programmer’s View
Programmer doesn’t need detailed understanding of architecture
  Instead, needs to know what instructions can be executed
Two levels of instructions:
  Assembly level
  Structured languages (C, C++, Java, etc.)
Most development today done using structured languages
  But, some assembly level programming may still be necessary
  Drivers: portion of program that communicates with and/or controls (drives) another device
    Often have detailed timing considerations, extensive bit manipulation
    Assembly level may be best for these

## Slide 30: Assembly-Level Instructions
opcode
operand1
operand2
opcode
operand1
operand2
opcode
operand1
operand2
opcode
operand1
operand2
...
Instruction 1
Instruction 2
Instruction 3
Instruction 4
Instruction Set
  Defines the legal set of instructions for that processor
    Data transfer: memory/register, register/register, I/O, etc.
    Arithmetic/logical: move register through ALU and back
    Branches: determine next PC value when not just PC+1

## Slide 31: Optimizing single-purpose processors
Optimization is the task of making design metric values the best possible
Optimization opportunities
  original program
  FSMD
  datapath
  FSM

## Slide 32: Optimizing the original program
Analyze program attributes and look for areas of possible improvement
  number of computations
  size of variable
  time and space complexity
  operations used
    multiplication and division very expensive

## Slide 33: Optimizing the original program (cont’)
0: int x, y;
1: while (1) {
2: while (!go_i);
3: x = x_i;
4: y = y_i;
5: while (x != y) {
6: if (x < y)
7: y = y - x;
else
8: x = x - y;
}
9: d_o = x;
}
0: int x, y, r;
1: while (1) {
2: while (!go_i);
// x must be the larger number
3: if (x_i >= y_i) {
4: x=x_i;
5: y=y_i;
}
6: else {
7: x=y_i;
8: y=x_i;
}
9: while (y != 0) {
10: r = x % y;
11: x = y;
12: y = r;
}
13: d_o = x;
}
original program
optimized program
replace the subtraction operation(s) with modulo operation in order to speed up program
GCD(42, 8) - 9 iterations to complete the loop
x and y values evaluated as follows : (42, 8), (43, 8), (26,8), (18,8), (10, 8), (2,8), (2,6), (2,4), (2,2).
GCD(42,8) - 3 iterations to complete the loop
x and y values evaluated as follows: (42, 8), (8,2), (2,0)

## Slide 35: Programmable Logic Device
Programmable Logic Device
  Programmable Logic Array, Programmable Array Logic, Field Programmable Gate Array
All layers already exist
  Designers can purchase an IC
  To implement desired functionality
    Connections on the IC are either created or destroyed to implement
Benefits
  Very low NRE costs
  Great time to market
Drawback
  High unit cost, bad for large volume
  Power
    Except special PLA
  slower
1600 usable gate, 7.5 ns
$7 list price

## Slide 36: Xilinx FPGA