## Slide 1: Chapter 4: Computing Platform
Embedded System Design

## Slide 2: Microcontrollers
Microprocessor
  CPU (on single chip)
Microcontroller
CPU + Timers + I/O (+RAM) (+ROM)
    Reduced chip count for board design
    Embedded system
    Today’s Technology:
      Surface Mount Device (SMD)
      Ball Grid Array (BGA)

## Slide 3
Data Bus
Data Memory
Program Memory
interrupts
Digital o/p
Analog o/p
Digital i/p
Analog i/p
INPUTS
OUTPUTS
Links to Other Systems
User Interface
Address Bus
CPU
Analog Front End
Digital i/p Ports
User Interface Modules
Digital o/p Ports
D/A,
Isolation..
Comms:
ASC, SSC, USB, IIC,
IrDA, etc.
Support:
Timers
Watchdog
3 of

## Slide 4: Two Memory Architectures
Processor
Program memory
Data memory
Processor
Memory
(program and data)
Harvard
Princeton
Princeton
  Fewer memory wires
Harvard
  Simultaneous program and data memory access

## Slide 5: A simple bus
bus structure
Processor
Memory
rd'/wr
enable
addr[0-11]
data[0-7]
bus
Wires:
  Uni-directional or bi-directional
  One line may represent multiple wires
Bus
  Set of wires with a single function
    Address bus, data bus
  Or, entire collection of wires
    Address, data and control
    Associated protocol: rules for communication

## Slide 6: Ports
Conducting device on periphery
Connects bus to processor or memory
Often referred to as a pin
  Actual pins on periphery of IC package that plug into socket on printed-circuit board
  Sometimes metallic balls instead of pins
  Today, metal “pads” connecting processors and memories within single IC
Single wire or set of wires with single function
  E.g., 12-wire address port
bus
Processor
Memory
rd'/wr
enable
addr[0-11]
data[0-7]
port

## Slide 7: Timing Diagrams
write protocol
rd'/wr
enable
addr
data
tsetup
twrite
Most common method for describing a communication protocol
Time proceeds to the right on x-axis
Control signal: low or high
  May be active low (e.g., go’, /go, or go_L)
  Use terms assert (active) and deassert
  Asserting go’ means go=0
Data signal: not valid or valid
Protocol may have subprotocols
  Called bus cycle, e.g., read and write
  Each may be several clock cycles
Read example
  rd’/wr set low,address placed on addr for at least tsetup time before enable asserted, enable triggers memory to place data on data wires by time tread
read protocol
rd'/wr
enable
addr
data
tsetup
tread

## Slide 8: Memory hierarchy
Want inexpensive, fast memory
Main memory
  Large, inexpensive, slow memory stores entire program and data
Cache
  Small, expensive, fast memory stores copy of likely accessed parts of larger memory
  Can be multiple levels of cache
Processor
Cache
Main memory
Disk
Tape
Registers

## Slide 9: Cache
Usually designed with SRAM
  faster but more expensive than DRAM
Usually on same chip as processor
  space limited, so much smaller than off-chip main memory
  faster access ( 1 cycle vs. several cycles for main memory)
Cache operation:
  Request for main memory access (read or write)
  First, check cache for copy
    cache hit
      copy is in cache, quick access
    cache miss
      copy not in cache, read address and possibly its neighbors into cache
Several cache design choices
  cache mapping, replacement policies, and write techniques

## Slide 10: Cache mapping
Far fewer number of available cache addresses
Are address’ contents in cache?
Cache mapping used to assign main memory address to cache address and determine hit or miss
Three basic techniques:
  Direct mapping
  Fully associative mapping
  Set-associative mapping
Caches partitioned into indivisible blocks or lines of adjacent memory addresses
  usually 4 or 8 addresses per line

## Slide 11: Cache-replacement policy
Technique for choosing which block to replace
  when fully associative cache is full
  when set-associative cache’s line is full
Direct mapped cache has no choice
Random
  replace block chosen at random
LRU: least-recently used
  replace block not accessed for longest time
FIFO: first-in-first-out
  push block onto queue when accessed
  choose block to replace by popping queue

## Slide 12: Cache write techniques
When written, data cache must update main memory
Write-through
  write to main memory whenever cache is written to
  easiest to implement
  processor must wait for slower main memory write
  potential for unnecessary writes
Write-back
  main memory only written when “dirty” block replaced
  extra dirty bit for each block set when cache block written to
  reduces number of slow main memory writes

## Slide 13: Memory: basic concepts
Stores large number of bits
  m x n: m words of n bits each
  k = Log2(m) address input signals
  or m = 2^k words
  e.g., 4,096 x 8 memory:
    32,768 bits
    12 address input signals
    8 input/output data signals
Memory access
  r/w: selects read or write
  enable: read or write only when asserted
  multiport: multiple accesses to different locations simultaneously
m × n memory
…
…
n bits per word
m words
enable
2k × n read and write memory
A0
…
r/w
…
Q0
Qn-1
Ak-1
memory external view

## Slide 14: Write ability/ storage permanence
Traditional ROM/RAM distinctions
  ROM
    read only, bits stored without power
  RAM
    read and write, lose stored bits without power
Traditional distinctions blurred
  Advanced ROMs can be written to
    e.g., EEPROM
  Advanced RAMs can hold bits without power
    e.g., NVRAM
Write ability
  Manner and speed a memory can be written
Storage permanence
  ability of memory to hold stored bits after they are written
Write ability and storage permanence of memories,
showing relative degrees along each axis (not to scale).
External
programmer
OR in-system,
block-oriented
writes, 1,000s
of cycles
Battery
life (10
years)
Write
ability
EPROM
Mask-programmed ROM
EEPROM
FLASH
NVRAM
SRAM/DRAM
Storage
permanence
Nonvolatile
In-system
programmable
Ideal memory
OTP ROM
During
fabrication
only
External
programmer,
1,000s
of cycles
External
programmer,
one time only
External
programmer
OR in-system,
1,000s
of cycles
In-system, fast
writes,
unlimited
cycles
Near
zero
Tens of
years
Life of
product

## Slide 15: Write ability
Ranges of write ability
  High end
    processor writes to memory simply and quickly
    e.g., RAM
  Middle range
    processor writes to memory, but slower
    e.g., FLASH, EEPROM
  Lower range
    special equipment, “programmer”, must be used to write to memory
    e.g., EPROM, OTP ROM
  Low end
    bits stored only during fabrication
    e.g., Mask-programmed ROM
In-system programmable memory
  Can be written to by a processor in the embedded system using the memory
  Memories in high end and middle range of write ability

## Slide 16: Storage permanence
Range of storage permanence
  High end
    essentially never loses bits
    e.g., mask-programmed ROM
  Middle range
    holds bits days, months, or years after memory’s power source turned off
    e.g., NVRAM
  Lower range
    holds bits as long as power supplied to memory
    e.g., SRAM
  Low end
    begins to lose bits almost immediately after written
    e.g., DRAM
Nonvolatile memory
  Holds bits after power is no longer supplied
  High end and middle range of storage permanence

## Slide 17: ROM: “Read-Only” Memory
Nonvolatile memory
Can be read from but not written to, by a processor in an embedded system
Traditionally written to, “programmed”, before inserting to embedded system
Uses
  Store software program for general-purpose processor
    program instructions can be one or more ROM words
  Store constant data needed by system
  Implement combinational circuit
2k × n ROM
…
Q0
Qn-1
A0
…
enable
Ak-1
External view

## Slide 18: Example: 8 x 4 ROM
Horizontal lines = words
Vertical lines = data
Lines connected only at circles
Decoder sets word 2’s line to 1 if address input is 010
Data lines Q3 and Q1 are set to 1 because there is a “programmed” connection with word 2’s line
Word 2 is not connected with data lines Q2 and Q0
Output is 1010
8 × 4 ROM
3×8 decoder
Q0
Q3
A0
enable
A2
word 0
word 1
A1
Q2
Q1
programmable connection
wired-OR
word line
data line
word 2
Internal view

## Slide 19: Implementing combinational function
Any combinational circuit of n functions of same k variables can be done with 2^k x n ROM
Truth table
Inputs (address) Outputs
a b c y z
0 0 0 0 0
0 0 1 0 1
0 1 0 0 1
0 1 1 1 0
1 0 0 1 0
1 0 1 1 1
1 1 0 1 1
1 1 1 1 1
0 0
0 1
0 1
1 0
1 0
1 1
1 1
1 1
z
y
c
enable
a
b
8×2 ROM
word 0
word 1
word 7

## Slide 20: Mask-programmed ROM
Connections “programmed” at fabrication
  set of masks
Lowest write ability
  only once
Highest storage permanence
  bits never change unless damaged
Typically used for final design of high-volume systems
  spread out NRE cost for a low unit cost

## Slide 21: OTP ROM: One-time programmable ROM
Connections “programmed” after manufacture by user
  user provides file of desired contents of ROM
  file input to machine called ROM programmer
  each programmable connection is a fuse
  ROM programmer blows fuses where connections should not exist
Very low write ability
  typically written only once and requires ROM programmer device
Very high storage permanence
  bits don’t change unless reconnected to programmer and more fuses blown
Commonly used in final products
  cheaper, harder to inadvertently modify

## Slide 22: EPROM: Erasable programmable ROM
.
(d)
(a)
(b)
source
drain
+15V
source
drain
0V
(c)
source
drain
floating gate
5-30 min
Programmable component is a MOS transistor
  Transistor has “floating” gate surrounded by an insulator
  (a) Negative charges form a channel between source and drain storing a logic 1
  (b) Large positive voltage at gate causes negative charges to move out of channel and get trapped in floating gate storing a logic 0
  (c) (Erase) Shining UV rays on surface of floating-gate causes negative charges to return to channel from floating gate restoring the logic 1
  (d) An EPROM package showing quartz window through which UV light can pass
Better write ability
  can be erased and reprogrammed thousands of times
Reduced storage permanence
  program lasts about 10 years but is susceptible to radiation and electric noise
Typically used during design development

## Slide 23: EEPROM: Electrically erasable programmable ROM
Programmed and erased electronically
  typically by using higher than normal voltage
  can program and erase individual words
Better write ability
  can be in-system programmable with built-in circuit to provide higher than normal voltage
    built-in memory controller commonly used to hide details from memory user
  writes very slow due to erasing and programming
    “busy” pin indicates to processor EEPROM still writing
  can be erased and programmed tens of thousands of times
Similar storage permanence to EPROM (about 10 years)
Far more convenient than EPROMs, but more expensive

## Slide 24: Flash Memory
Extension of EEPROM
  Same floating gate principle
  Same write ability and storage permanence
Fast erase
  Large blocks of memory erased at once, rather than one word at a time
  Blocks typically several thousand bytes large
Writes to single words may be slower
  Entire block must be read, word updated, then entire block written back
Used with embedded systems storing large data items in nonvolatile memory
  e.g., digital cameras, TV set-top boxes, cell phones

## Slide 25: RAM: “Random-access” memory
Typically volatile memory
  bits are not held without power supply
Read and written to easily by embedded system during execution
Internal structure more complex than ROM
  a word consists of several memory cells, each storing 1 bit
  each input and output data line connects to each cell in its column
  rd/wr connected to every cell
  when row is enabled by decoder, each cell has logic that stores input data bit when rd/wr indicates write or outputs stored bit when rd/wr indicates read
enable
2k × n read and write memory
A0
…
r/w
…
Q0
Qn-1
Ak-1
external view
4×4 RAM
2×4 decoder
Q0
Q3
A0
enable
A1
Q2
Q1
Memory cell
I0
I3
I2
I1
rd/wr
To every cell
internal view

## Slide 26: Basic types of RAM
SRAM: Static RAM
  Memory cell uses flip-flop to store bit
  Requires 6 transistors
  Holds data as long as power supplied
DRAM: Dynamic RAM
  Memory cell uses MOS transistor and capacitor to store bit
  More compact than SRAM
  “Refresh” required due to capacitor leak
    word’s cells refreshed when read
  Typical refresh rate 15.625 microsec.
  Slower to access than SRAM
memory cell internals
Data
W
Data'
SRAM
Data
W
DRAM

## Slide 27: Ram variations
PSRAM: Pseudo-static RAM
  DRAM with built-in memory refresh controller
  Popular low-cost high-density alternative to SRAM
NVRAM: Nonvolatile RAM
  Holds data after external power removed
  Battery-backed RAM
    SRAM with own permanently connected battery
    writes as fast as reads
    no limit on number of writes unlike nonvolatile ROM-based memory
  SRAM with EEPROM or flash
    stores complete RAM contents on EEPROM or flash before power turned off

## Slide 28: Example: HM6264 & 27C256 RAM/ROM devices
Low-cost low-capacity memory devices
Commonly used in 8-bit microcontroller-based embedded systems
First two numeric digits indicate device type
  RAM: 62
  ROM: 27
Subsequent digits indicate capacity in kilobits
Device Access Time (ns) Standby Pwr. (mW) Active Pwr. (mW) Vcc Voltage (V)
HM6264 85-100 .01 15 5
27C256 90 .5 100 5
22
20
data<7…0>
addr<15...0>
/OE
/WE
/CS1
CS2
HM6264
11-13, 15-19
2,23,21,24,
25, 3-10
22
27
20
26
data<7…0>
addr<15...0>
/OE
/CS
27C256
11-13, 15-19
27,26,2,23,21,
24,25, 3-10
block diagrams
device characteristics
timing diagrams
data
addr
OE
/CS1
CS2
Read operation
data
addr
WE
/CS1
CS2
Write operation

## Slide 39
Schematic
CPU
Memory
Permanent Memory
Input device
(keyboard)
Sensors to measure physical values
Actuators to control physical things
Output device (screen)
bus
program
Need to know:
Digital Logic, Electrical Circuits, Computer Architecture

## Slide 40: Timers, counters, watchdog timers
Timer: measures time intervals
  To generate timed output events
    e.g., hold traffic light green for 10 s
  To measure input events
    e.g., measure a car’s speed
Based on counting clock pulses
    E.g., let Clk period be 10 ns
    And we count 20,000 Clk pulses
    Then 200 microseconds have passed
    16-bit counter would count up to 65,535*10 ns = 655.35 microsec., resolution = 10 ns
    Top: indicates top count reached, wrap-around
16-bit up counter
Clk
Cnt
Basic timer
Top
Reset
16

## Slide 41: Counters
Counter: like a timer, but counts pulses on a general input signal rather than clock
  e.g., count cars passing over a sensor
  Can often configure device as either a timer or counter
16-bit up counter
Clk
16
Cnt_in
2x1 mux
Mode
Timer/counter
Top
Reset
Cnt

## Slide 42: Watchdog timer
scalereg
checkreg
timereg
to system reset
or
interrupt
osc
clk
prescaler
overflow
overflow
/* main.c */
main(){
wait until card inserted
call watchdog_reset_routine
while(transaction in progress){
if(button pressed){
perform corresponding action
call watchdog_reset_routine
}
/* if watchdog_reset_routine not called every < 2 minutes, interrupt_service_routine is called */
}
watchdog_reset_routine(){
/* checkreg is set so we can load value into timereg. Zero is loaded into scalereg and 11070 is loaded into timereg */
checkreg = 1
scalereg = 0
timereg = 11070
}
void interrupt_service_routine(){
eject card
reset screen
}
Must reset timer every X time unit, else timer generates a signal
Common use: detect failure, self-reset
Another use: timeouts
  e.g., ATM machine
  16-bit timer, 2 microsec. resolution
  timereg value = 2*(216-1)–X = 131070–X
  For 2 min., X = 120,000 microsec.

## Slide 43: LCD controller
E
R/W
RS
DB7–DB0
LCD controller
communications bus
microcontroller
8
void WriteChar(char c){
RS = 1; /* indicate data being sent */
DATA_BUS = c; /* send data to LCD */
EnableLCD(45); /* toggle the LCD with appropriate delay */
}

## Slide 44: Keypad controller
N1
N2
N3
N4
M1
M2
M3
M4
key_code
keypad controller
k_pressed
key_code
4
N=4, M=4

## Slide 45
The Seven Segment Display
Display Controller
Counter
Clock
0000
0001
0010
0011
0100
…..

## Slide 46
GPS Navigator
Complex system with many components
  GPS Radio
  GPS signal processor
  Map database
  Processor to control display and compute routes, locations, points of interest
  Video image processor to control actual screen
May contain several different CPUs in one package

## Slide 47
GPS Radio
Receives data from several satellites, converts RF to digital signals
  Separate for each satellite
Radio
receiver
circuitry
Signals (digital) from each satellite on separate wires
A set of at least 24 Medium Earth Orbit satellites that transmit precise microwave signals,
A GPS receiver can determine its location, speed, direction, and time.

## Slide 48
GPS signal processor
Correlates satellite signals
  Computes timing differences
  “triangulates” location
GPS data processor
Current location in latitude and longitude
Need to know:
Radio, Signal processing, Algorithms

## Slide 49
GPS Navigator
The user interface – show location on map and provide useful other information
GPS Computer
Display Processor
MAP database
Touch Sensor
Need to know:
Computer Graphics, Graph Theory

## Slide 50: Analog-to-digital converters
proportionality
Vmax = 7.5V
0V
1111
1110
0000
0010
0100
0110
1000
1010
1100
0001
0011
0101
0111
1001
1011
1101
0.5V
1.0V
1.5V
2.0V
2.5V
3.0V
3.5V
4.0V
4.5V
5.0V
5.5V
6.0V
6.5V
7.0V
analog to digital
4
3
2
1
t1
t2
t3
t4
0100
1000
0110
0101
time
analog input (V)
Digital output
digital to analog
4
3
2
1
0100
1000
0110
0101
t1
t2
t3
t4
time
analog output (V)
Digital input

## Slide 51: Digital-to-analog conversion using successive approximation
Given an analog input signal whose voltage should range from 0 to 15 volts, and an 8-bit digital encoding, calculate the correct encoding for 5 volts. Then trace the successive-approximation approach to find the correct encoding.
5/15 = d/(28-1)
d= 85
Successive-approximation method
0
1
0
0
0
0
0
0
Encoding: 01010101
½(Vmax – Vmin) = 7.5 volts
Vmax = 7.5 volts.
½(7.5 + 0) = 3.75 volts
Vmin = 3.75 volts.
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
½(7.5 + 3.75) = 5.63 volts
Vmax = 5.63 volts
½(5.63 + 3.75) = 4.69 volts
Vmin = 4.69 volts.
0
1
0
1
0
0
0
0
½(5.63 + 4.69) = 5.16 volts
Vmax = 5.16 volts.
0
1
0
1
0
0
0
0
½(5.16 + 4.69) = 4.93 volts
Vmin = 4.93 volts.
0
1
0
1
0
1
0
0
½(5.16 + 4.93) = 5.05 volts
Vmax = 5.05 volts.
0
1
0
1
0
1
0
0
½(5.05 + 4.93) = 4.99 volts
0
1
0
1
0
1
0
1