## Slide 1: Chapter 5: Program Design Analysis
Embedded System Design

## Slide 2: Development Environment
Development processor
  The processor on which we write and debug our programs
    Usually a PC
Target processor
  The processor that the program will run on in our embedded system
    Often different from the development processor
Development processor
Target processor

## Slide 3: Operating System
Optional software layer providing low-level services to a program (application).
  File management, disk access
  Keyboard/display interfacing
  Scheduling multiple programs for execution
    Or even just multiple threads from one program
  Program makes system calls to the OS

## Slide 4: Testing and Debugging
Implementation Phase
Implementation Phase
Verification Phase
Verification
Phase
Emulator
Debugger/ ISS
Programmer
Development processor
(a)
(b)
External tools
ISS
  Gives us control over time – set breakpoints, look at register values, set values, step-by-step execution, ...
  But, doesn’t interact with real environment
Download to board
  Use device programmer
  Runs in real environment, but not controllable
Compromise: emulator
  Runs in real environment, at speed or near
  Supports some controllability from the PC

## Slide 5: Instruction Set Simulator For A Simple Processor
#include <stdio.h>
typedef struct {
unsigned char first_byte, second_byte;
} instruction;
instruction program[1024]; //instruction memory
unsigned char memory[256]; //data memory
void run_program(int num_bytes) {
int pc = -1;
unsigned char reg[16], fb, sb;
while( ++pc < (num_bytes / 2) ) {
fb = program[pc].first_byte;
sb = program[pc].second_byte;
switch( fb >> 4 ) {
case 0: reg[fb & 0x0f] = memory[sb]; break;
case 1: memory[sb] = reg[fb & 0x0f]; break;
case 2: memory[reg[fb & 0x0f]] =
reg[sb >> 4]; break;
case 3: reg[fb & 0x0f] = sb; break;
case 4: reg[fb & 0x0f] += reg[sb >> 4]; break;
case 5: reg[fb & 0x0f] -= reg[sb >> 4]; break;
case 6: pc += sb; break;
default: return –1;
}
}
return 0;
}
int main(int argc, char *argv[]) {
FILE* ifs;
If( argc != 2 ||
(ifs = fopen(argv[1], “rb”) == NULL ) {
return –1;
}
if (run_program(fread(program,
sizeof(program) == 0) {
print_memory_contents();
return(0);
}
else return(-1);
}

## Slide 6: Example: parallel port driver
Using assembly language programming we can configure a PC parallel port to perform digital I/O
  write and read to three special registers to accomplish this table provides list of parallel port connector pins and corresponding register location
  Example : parallel port monitors the input switch and turns the LED on/off accordingly
LPT Connection Pin
I/O Direction
Register Address
1
Output
0th bit of register #2
2-9
Output
0th bit of register #2
14,16,17
Output
1,2,3th bit of register #2
10,11,12,13,15
Input
6,7,5,4,3th bit of register #1

## Slide 7: Optimizing single-purpose processors
Optimization is the task of making design metric values the best possible
Optimization opportunities
  original program
  FSMD
  datapath
  FSM

## Slide 8: Optimizing the original program
Analyze program attributes and look for areas of possible improvement
  number of computations
  size of variable
  time and space complexity
  operations used
    multiplication and division very expensive

## Slide 9: Optimizing the original program (cont’)
0: int x, y;
1: while (1) {
2: while (!go_i);
3: x = x_i;
4: y = y_i;
5: while (x != y) {
6: if (x < y)
7: y = y - x;
else
8: x = x - y;
}
9: d_o = x;
}
0: int x, y, r;
1: while (1) {
2: while (!go_i);
// x must be the larger number
3: if (x_i >= y_i) {
4: x=x_i;
5: y=y_i;
}
6: else {
7: x=y_i;
8: y=x_i;
}
9: while (y != 0) {
10: r = x % y;
11: x = y;
12: y = r;
}
13: d_o = x;
}
original program
optimized program
replace the subtraction operation(s) with modulo operation in order to speed up program
GCD(42, 8) - 9 iterations to complete the loop
x and y values evaluated as follows : (42, 8), (43, 8), (26,8), (18,8), (10, 8), (2,8), (2,6), (2,4), (2,2).
GCD(42,8) - 3 iterations to complete the loop
x and y values evaluated as follows: (42, 8), (8,2), (2,0)

## Slide 10: Memory Management Unit (MMU)
Duties of MMU
  Handles DRAM refresh, bus interface and arbitration
  Takes care of memory sharing among multiple processors
  Translates logic memory addresses from processor to physical memory addresses of DRAM
Modern CPUs often come with MMU built-in
Single-purpose processors can be used

## Slide 11: Periodic, Sporadic, Aperiodic Tasks
Periodic task:
  We associate a period pi with each task Ti.
  pi is the interval between job releases.
Sporadic and Aperiodic tasks: Released at arbitrary times.
  Sporadic: Has a hard deadline.
  Aperiodic: Has no deadline or a soft deadline.

## Slide 12: Examples
= job release
= job deadline
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18
A periodic task Ti with ri = 2, pi = 5, ei = 2, Di =5 executes like this:

## Slide 13: Classification of Scheduling Algorithms
All scheduling algorithms
static scheduling
(or offline, or clock driven)
dynamic scheduling
(or online, or priority driven)
static-priority
scheduling
dynamic-priority
scheduling

## Slide 14: Real-Time Systems
Timing requirements
  meeting deadlines
Periodic and aperiodic tasks
Shared resources
Interrupts
Notes: 14
4
Real-time systems generally consist of independently schedulable threads of control called tasks. Here the term task does not necessarily mean an Ada task; rather, a schedulable unit of processing, like a process or thread.
Tasks may be periodic or aperiodic
Periodic tasks are initiated at regular intervals.
Aperiodic tasks are initiated at irregular intervals.
Tasks have deadlines which may be hard or soft.
Failure to meet hard deadlines results in system failure.
Failure to meet soft deadlines degrades system performance.
For the purposes of this workshop, we assume:
Deadline for periodic task is hard (either at or before end of period).
Deadline for aperiodic task may be hard or soft.
Some investigators further categorize tasks as being critical or non-critical. Failure of a critical task to meet a hard deadline (if one exists) is considered catastrophic

## Slide 15: What’s Important in Real-Time
  schedulability is the ability of tasks to meet all hard deadlines
  latency is the worst-case system response time to events
  stability in overload means the system meets critical deadlines even if all deadlines cannot be met
 | Time-Sharing Systems | Real-Time Systems
Capacity | High throughput | Schedulability
Responsiveness | Fast average response | Ensured worst-case response
Overload | Fairness | Stability

## Slide 16: Scheduling Policies
CPU scheduling policy: a rule to select task to run next
  cyclic executive
  rate monotonic/deadline monotonic
  earliest deadline first
  least laxity first
Assume preemptive, priority scheduling of tasks
  analyze effects of non-preemption later
Notes: 16
6
Real-time systems use a variety of scheduling policies.
Cyclic executive - where all work (tasks) are fit into a common period (major frame) and executed non-preemptively.
Rate monotonic - preemptive scheduling where tasks are assigned priorities based on rates, or periods.
Deadline monotonic - preemptive execution where tasks are assigned priorities based on fixed deadlines.
Earliest deadline first - preemptive scheduling, where tasks are assigned priorities dynamically, based on closeness of current deadlines.
Least laxity first - preemptive scheduling, where tasks are assigned priorities dynamically, based on the amount of slack time that remains between time needed to complete work and time to the deadline.
Criteria for real-time scheduling policies:
Achieve high utilization and still guarantee hard deadlines.
Provide fast aperiodic response and still guarantee hard deadlines.
Low overhead: fixed versus dynamic priorities; dynamic policies tend to have higher overhead, since they may reorder the run queue at each scheduling decision.
This tutorial will first assume preemptive scheduling, then consider effects of non-preemption.

## Slide 17: Rate Monotonic Scheduling (RMS)
Priorities of periodic tasks are based on their rates: highest rate gets highest priority.
Theoretical basis
  optimal fixed scheduling policy (when deadlines are at end of period)
  analytic formulas to check schedulability
Must distinguish between scheduling and analysis
  rate monotonic scheduling forms the basis for rate monotonic analysis
  however, we consider later how to analyze systems in which rate monotonic scheduling is not used
  any scheduling approach may be used, but all real-time systems should be analyzed for timing
Notes: 17
7
In 1973, Liu and Leyland published a paper called “ Scheduling Algorithms for Multiprogrammimg in a Hard-Real-Time Environment.” In this paper, they introduce the rate monotonic scheduling (RMS) algorithm. The RMS algorithm is an optimal static-priority scheduling algorithm, which gives higher priority to tasks with shorter periods (in other words, higher priority to tasks with higher frequencies, or rates).
It is important to emphasize that tasks are assigned priorities based strictly on their periods. Semantic importance does not play a role in priority assignment.
The algorithm is optimal in the sense that a task set that cannot meet its deadlines with a rate monotonic priority assignment will not be able to be scheduled with any fixed-priority assignment.
The original 1973 work on rate monotonic scheduling theory assumed that RMS was used and all tasks were periodic and non-interacting. Given these assumptions, a simple formula could be used to check for task schedulability, i.e. if each task is guaranteed to meet all its deadlines.
It is important to distinguish between rate monotonic scheduling (RMS) and rate monotonic analysis (RMA). Although the analysis approach has grown out of RMS theory, RMA can be done on a system even if RMS is not the scheduling approach used

## Slide 18: Rate Monotonic Analysis (RMA)
Rate-monotonic analysis is a set of mathematical techniques for analyzing sets of real-time tasks.
Basic theory applies only to independent, periodic tasks, but has been extended to address
  priority inversion
  task interactions
  aperiodic tasks
Focus is on RMA, not RMS
Notes: 18
8
RMA is a mathematical approach for analyzing real-time tasks to determine their schedulability. Again, the original theory was only able to analyze independent, periodic tasks. However, the basic theory has been extended to analyze cases that include inversion, task interactions, and aperiodic tasks.
In this tutorial, we will first introduce the mechanics of the analysis based on the original RMS theory assumptions, which are very restrictive. We will then systematically relax the assumptions and extend the basic theory.
Remember that the analysis can be done on systems that are scheduled by other algorithms. Again, this is the strength in rate monotonic theory. The analysis can be applied to any system, providing insight to its timing behavior. From now on, our focus is on rate monotonic analysis (RMA) of systems, which may or may not use the rate monotonic scheduling (RMS) algorithm.
In this tutorial we will cover priority inversion. We will cover task interactions and aperiodics as time allows

## Slide 19: Why Are Deadlines Missed?
For a given task, consider
  preemption: time waiting for higher priority tasks
  execution: time to do its own work
  blocking: time delayed by lower priority tasks
The task is schedulable if the sum of its preemption, execution, and blocking is less than its deadline.
Focus: identify the biggest hits among the three and reduce, as needed, to achieve schedulability
Notes: 19
9
Note:
For a task to meet its deadline, it must accommodate
Preemption from higher-priority tasks,
Its own execution time, and
Delays caused by lower-priority tasks (known as priority inversion or blocking).
Remember that higher-priority tasks, from a rate monotonic perspective, are those with higher rates (or shorter periods). These can occur more than once in a task’s period. A task’s execution occurs once during its period. And blocking can occur at most once during the task’s period; blocking comes from lower-priority tasks, those that have slower rates (or longer periods).
Preemption and execution are unavoidable. If these exceed capacity, one is faced with a classical throughput problem and the only remedy is to reduce the workload (which means changing the system requirements) or to increase the capacity by using a faster computer. Experience has shown that priority inversion (blocking), delay from lower-priority tasks, is a major source of missed deadlines. So we focus on identifying sources of priority inversion and try to reduce their blocking effects to enhance schedulability.

## Slide 20: Rate Monotonic Theory - Experience
Supported by several standards
  POSIX Real-time Extensions
    Various real-time versions of Linux
  Java (Real-Time Specification for Java and Distributed Real-Time Specification for Java)
  Real-Time CORBA
  Real-Time UML
  Ada 83 and Ada 95
  Windows 95/98
  …
Notes: 20
22
IBM System Integration Division (SID) Manassas developed and delivered a “schedulable” real-time network to the Navy.
RMA was successfully used by IBM to improve the performance of the BSY-1 Trainer while under development. (A case study in this tutorial reviews this.)
RMA principles were used to design real-time scheduling support in the IEEE FutureBus+ standard.
The NASA Space Station program has decided to adopt RMA in their development effort. They are currently implementing management practices for the use of RMA.
The European Space Agency is requiring that RMS theory be used as the baseline theory for its hard real-time operating system (OS) contract.
Various software vendors are offering products and services that support RMA: Compiler and runtime vendors; Real-time operating system vendors; Commercial training firms.
IBM's response-time analysis effort is using several of the same techniques detailed in the handbook to determine which parts of the system will meet its response-time requirements, even under worst-case system conditions, and which need modification to meet requirements. The analysis is being done by several IBM engineers on an initial release of over 1 million lines of code, allowing its response-time characteristics to be established early enough to take corrective action before full-scale testing and deployment. The analysis effort is expected to be a continuous activity throughout the development and deployment of the system.